## Slide 1: Separation methods in medicine
LIQUID
CHROMATOGRAPHY
MASS SPECTROMETRY

## Slide 2
Disclaimer
Due to a very limited time I’ve been given for this topic, the theory on LC—MS is hardly oversimplified !!!
For those, who would be interested, more correct and comprehensive information can be found e.g. there:
https://cdn.intechopen.com/pdfs/29014/InTech-Principles_and_applications_of_lc_ms_ms_for_the_quantitative_bioanalysis_of_analytes_in_various_biological_samples.pdf

## Slide 3: Introduction
Therapeutic Drug Monitoring :: TDM
Diagnosis of inherited metabolic disorders
Toxicological screening
Metabolomics, lipidomics, proteomics, ...
Sample collection & treatment
LC-MS analysis
Data processing
&
interpretation
Quantitative and qualitative analysis of compounds in biological material

## Slide 4: Why do we need separation?
Biological samples complexity
Thousands of compounds
Broad range of MW
Low & high molecular compounds
For more reliable
and precise quantification or identification of compounds
Many interfering compounds
Signal overlaps
Matrix effects
Orders of magnitude differences in concentration
TAG
1.0 mmol/L
Estradiol in man 50 pmol/L

## Slide 5: Separation using liquid chromatography (LC)
Separation takes place based on the distribution of substances between two mutually immiscible phases: (l)-(s), nebo (l)-(l)
(s)
(l)
Can be used for molecules with broad range of MW
LC is the most common chromatographic method in clinical laboratory

## Slide 6: Phases in LC
ALWAYS 2 immiscible phases !!!
stationary phase is solid
mobile phase is liquid

## Slide 7: Stationary phase
Stationary phase :: is filled into chromatographic columns
Column :: stainless steel „pipe“ filled with suitable stationary phase - sorbent
Sorbent :: porous spheric particles made of silica gel, usually further chemically modified at the surface
~ 2 um
The sorbent provides interaction with the separated substances

## Slide 8: Mobile phase
The sample intended for separation is injected into its flow.
The individual components of the sample are carried through the column, where they are separated based on their physico-chemical properties.
The mobile phase ensures interaction with the separated substances and carries them through the chromatographic system.
In bioanalysis, mostly organic solvents miscible with water are used (methanol, acetonitrile, isopropanol) + water.

## Slide 9: Basic configuration of liquid chromatograph
mobile
phase
pump of
mobile phase
column
filled with a stationary phase
detector
computer
waste
sample injection

## Slide 10: Principle of on-column separation
compound B
compound A
mixture A + B
mobile phase flow
efluent

## Slide 11
compound B
compound A
stationary
phase
stationary
phase
mobile
phase
higher affinity to a stat. phase
longer time on column
higher retention
= longer retention time tR
Comp. A
Left the column 2nd
higher affinity to a mobile phase
shorter time on column
lower retention
= shorter retention time tR
Comp. B
Left the column 1st

## Slide 12: Detection of separated compounds
In order to determine what is leaving the chromatograph after separation, we must be able to detect the substances in the column effluent
Common modes of detection:
Light absorption in UV/VIS
Fluorescence
Mass spectrometry detection
Chromatograph
Mass spectrometer
efluent = liquid leaving a column

## Slide 13: Chromatogram – record of chromatographic separation
Retention time tR
Response
tR1
tR2
tR3
tR4
Retention time – tR
Qualitative information
Peak area – A
Quantitative information
A1
A2
A3
A4
Cmpnd 1
Cmpnd 4
Cmpnd 2
Cmpnd 3
Sometimes the peak height is used as quantitative information
h1

## Slide 14: Example of real chromatograms
tR (min)
Response
tR (min)
Response

## Slide 15: Mass spectrometry (MS)
Mass spectrometry makes it possible to determine the mass-to-charge ratio (m/z) of ions moving in an electric or magnetic field and their relative abundance.
Basic prerequisite for the detection of a substance using MS:
Analyte can be transferred into gas phase
The analyte does not decompose during transfer to the gas phase
The analyte can form ions in the gas phase
MS measures „weight“ of the molecules
Notes: 12 minut

## Slide 16: Basic principle of MS
Ion optics
Ion source
Mass analyzer
Detector of incoming ions
Ions with a different m/z
low m/z
high m/z
N
S

## Slide 17: Mass spectrum
Intensity %
m/z
50
100
150
200
250
300
350
400
450
500
550
100
80
60
40
20
490
397
361
132
82
102
68
153
Each peak in the mass spectrum corresponds to an ion with a specific m/z value.
The intensity of the peaks indicates the relative number of these ions detected.
Some information about the structure and composition of the analyzed substance can be obtained from the spectrum.
Record of the m/z ratio (“mass” of the ion) vs. signal intensity

## Slide 18: LC and MS coupling
The combination of these two techniques is commonly abbreviated as LC-MS.
Ion source
Nebulization of the liquid effluent from the column
Drying and aerosol formation
Charging of molecules
A wide variety of designs
At present, the most common is the so-called electrospray – ESI
At first glance “simple” – but a fundamental problem had to be solved: converting liquid mobile phase into the gaseous state and ionizing the molecules.
Notes: 5 minut

## Slide 19: Pros & cons of mass spectrometric detection
Pros
High selectivity
High sensitivity,
Possibility of substance identification
Versatility
Cons
Extremely expensive instrumentation
High operating costs
High demands on staff expertise
Susceptibility to matrix effects
Lower response stability
Notes: 12 minut

## Slide 20: What an LC-MS record looks like
m/z
Response
Retention time
Response
Retention time

## Slide 21: Advantages of MS compared to conventional detectors
Better selectivity
Facilitation of substance identification
Higher sensitivity

## Slide 22: Selectivity
EIC1
EIC2
EIC3
EIC4
Response
Retention time tR
Response
Retention time tR
UV/VIS detector
MS detector:
Extracted Ion Currents
EIC

## Slide 23: Sensitivity
UV/VIS detector
Detection limit  25 ng/mL (2.5 × 10-8 ng/mL)
MS detector
Detection limit  100 fg/mL (1.0 × 10-13 ng/mL)
Metamphetamine
190 m

## Slide 24: Compound identification using HRMS
High-Resolution Mass Spectrometry (HRMS)
Advanced mass spectrometry method
Allows measurement of m/z with very high accuracy and resolution
Enables differentiation of compounds with nearly identical masses
More reliable identification of unknown substances even in complex mixtures

## Slide 25: What can be inferred from an (HR)MS spectrum
Monoisotopic mass  molecular formula of the compound, molecular weight
Shape of isotopic cluster  number of carbons, presence of Cl, Br, S
RDBE :: Ring Double Bond Equivalent  minimum sum of double bonds and rings in the molecule
Fragmentation profile  information about molecular structure

## Slide 26: Clinical applications of LC-MS on selected practical examples
Newborn screening of inherited metabolic disorders
Personalized pharmacotherapy
    Monitoring of pharmacokinetics and therapeutic levels
    Determination of biomarkers of treatment efficacy and toxicity
    Pharmacogenomics in combination with phenotyping
    Toxicological screening
  Omics methods for the search of new biochemical markers
Notes: 12 minut

## Slide 27: Newborn screening for inherited metabolic disorders

## Slide 28
Department of Clinical Biochemistry, University Hospital Olomouc :: Prof. Friedecký
Analysis from a Dried Blood Spot (DBS)
Sampling between the 48th and 72nd hour of life from the newborn’s heel
Analysis using tandem mass spectrometry
prof. Friedecký
FN Olomouc

## Slide 29
Faty acids
Medium-chain acyl-CoA dehydrogenase deficiency
Long-chain L-3-hydroxyacyl-CoA dehydrogenase deficiency
Very long-chain acyl-CoA dehydrogenase deficiency
Carnitine palmitoyltransferase I deficiency
Carnitine palmitoyltransferase II deficiency
Carnitine-acylcarnitine translocase deficiency
Amin acids
Fenylketonuria
Hyperfenylalaninemia
Argininemia
Citrulinemia type I
Leucinosis
Homocystinuria
Glutaral aciduria type I
Isovalerate aciduria
In the Czech Republic, LC-MS is used for large-scale screening of neonatal metabolic disorders:
Phenylketonuria – autosomal recessive with an incidence in the Czech Republic of approximately 1:6000
Fenylalanin hydroxylase
Phe
Tyr
Phenyl pyruvate
Phenylalanin accumulation
CNS damage
Mental retardation

## Slide 30: Personalised pharmacotherapy

## Slide 31
Monitoring of pharmacokinetics and therapeutic levels
Pharmacogenomics in combination with phenotyping
Determination of disease biomarkers, treatment efficacy, and toxicity

## Slide 32
toxic
therapeutic
sub-therapeutic
time
Plasmatic konc.
time
Plasmatic konc.
toxic
therapeutic
sub-therapeutic
Wide therapeutic window
Narrow therapeutic window
drug
t0 Drug taken oraly
tmax maximum plasma concentration
Maximum plasma concentration
reaching toxic levels

## Slide 33
toxic
therapeutic
sub-therapeutic
Narrow therapeutic window
:: repeated administration
:: slow metabolizer
time
toxic
sub-therapeutic
therapeutic
Analysis of drug plasmatic conc.
Dose adjustment
time
Plasmatic konc.

## Slide 34
Dose adjustment
Therapeutic
Drug
Monitoring
Sample collection
Interpretation & evaluation by clinicist
Sample analysis
Therapeutic drug monitoring - TDM

## Slide 35
In more severe forms of Crohn’s disease, azathioprine / 6-mercaptopurine (MP) is used to maintain remission.
Genetic polymorphism of TPMT – some patients are potentially at risk of serious adverse effects.
In 20–30% of patients, long-term administration of MP does not lead to a clear clinical treatment effect.
Treatmentfailure?
Patient’s non-compliance ?
Can the treatment be initiated?
Practical example: Pharmacotherapy with 6-mercaptopurine in patients with Crohn’s disease – TDM and phenotyping
doc. Hroch
LF Hradec Králové
Notes: TPMT = thiopurinmethyltransferáza – hlavní detoxikační enzym v biotransformaci 6-merkaptopurinu

## Slide 36
Screening for TPMT deficient patients
Risk of myelotoxicity caused by high concentrations of the active metabolite thioguanine
Performed before the initiation of pharmacotherapy
                Screening for non-compliant patients
                With standard laboratory tests, it is quite difficult to determine whether there has been an objective treatment failure or merely patient non-compliance
Before the therapy
In course of the therapy

## Slide 37
Chart: t [day]
| 0 | 7 | 14 | 44 | 72 | 121 | 212 | 303 | 401
6-TG | 0 | 5.5701 | 11.097 | 15.1459 | 18.7654 | 14.0147 | 14.1655 | 11.9221 | 16.6229
6-MeMP | 0 | 1.9495 | 3.9023 | 4.6599 | 3.5374 | 7.5213 | 5.7613 | 6.9338 | 5.9468
Chart: t [day]
| 0 | 6 | 13 | 41 | 62 | 160 | 258
6-TG | 0 | 1.0301 | 3.2295 | 2.0026 | 2.9825 | 0 | 0
6-MeMP | 0 | 21.2914 | 22.7337 | 2.9117 | 3.2224 | 2.5615 | 0
Chart: odběr
| 1 | 2 | 3 | 4 | 5 | 6
6-TG | 1.3784 | 1.9842 | 1.4825 | 0 | 0.80862 | 0
6-MeMP | 2.9802 | 1.7417 | 2.5327 | 1.2814 | 1.9463 | 0
Chart: odběr
| 1 | 2 | 3 | 4
6-TG | 2.5565 | 2.4618 | 2.4428 | 3.2071
6-MeMP | 84.7272 | 108.1499 | 93.4481 | 86.4324
Patient with a low activity of TPMT
Patient on long-term therapy: irregular use and discontinuation pharmacotherapy
Patient on long-term therapy: treatment failure
6-thioguanin
6-methylmerkaptopurin
Poor adherence to treatment: discontinuation of pharmacotherapy

## Slide 38
Drugs for which plasma levels are routinely monitored using LC-MS

## Slide 39: Practical example: Determination of disease severity biomarkers Intrahepatic cholestasis of pregnancy (ICP)
Evaluation of the severity of cholestasis and the effect of pharmacological intervention
Determination of BAs from body fluids and tissues in model systems of intra- and extrahepatic cholestasis in rats
Collaboration with the University Hospital Olomouc
Screening of ICP
Determination of BAs profiles from blood and urine samples
Lipidomic analysis of bile acids (BAs)
Basic research
Clinical research

## Slide 40: Toxicologic screening

## Slide 41
Forensic toxicology
Screening for new illicit drugs
Detection and quantification of narcotic and psychotropic substances
Occupational toxicology
Monitoring of workers’ exposure to industrial chemicals
Monitoring of poisonings by drugs and poisons
Clinical toxicology
Doping control
Doping control of prohibited substances and their metabolites
Toxicologic screening
60 mm
Visualization of the lethal dose for selected hard drugs

## Slide 42
TIC
EIC
m/z 150.1277
Zdroj: FNHK – Ústav klinické biochemie a diagnostiky
Intoxication with METAMPHETAMIN ! was detected using LC-HRMS
LC-HRMS method for screening of 1600 compounds:
Most of the pharmaceuticals available on our market
Most common and less common drugs, pesticides, and industrial substances
3yo patient was admitted to the University Hospital with suspected intoxication
Practical example: Intoxication of a three-year-old boy
Department of Clinical and Forensic Toxicology at University Hospital Hradec Králové

## Slide 43: Omics

## Slide 44
Lipidomics
Metabolomics
Glycomics
Proteomics
Omics methods currently have a leading position in the search for new biochemical markers of serious diseases.
Multidisciplinary issue
Usually long-term research involving experts from a wide range of specializations
Medicine
Biostatistics
Bioinformatics
Molecular biology & genetics
Biochemistry
Analytical chemistry

## Slide 45
Practical example: Early diagnosis of pancreatic tumors using lipidomic analysis of a blood sample
M. Holčapek et al. Nature Communications. 2022 Jan 10;13:124.
The method is patented in the Czech Republic, Europe, Japan, and the USA
Lipidomic analysis
Fosfatidylinositols
Ceramides
Lysofosfatidylcholiny
Sfingomyelins
Fosfatidylcholines
Triacylglycerols
Set of lipid markers
Lipidome analysis using HILIC-MS/MS or UHPSFC–MS/MS
Dysregulation of selected lipids from different classes was identified
Decrease or increase in conc. compared to physiological values.
In most cases, they contain very long-chain fatty acids.
prof. Holčapek and his team at University of Pardubice

## Slide 46: Conclusion
Main idea: LC-MS combines efficient substance separation with sensitive and selective detection  analysis selectivity, sensitivity and reliability improvement
Indispensable for modern laboratory medicine.
Personalized medicine, TDM, omics methods in the search for disease biomarkers, toxicology, etc.
Notes: 3 minuty