## Slide 1: Chromatographic Methods – Worksheet
Solution

## Slide 2: Task 1 (qualitative analysis of the sample):
Imagine you work at the Department of Clinical Toxicology of the University Hospital and need to provide a report to the attending physician. You have a pre-measured chromatogram of reference standards (Appendix 1A) and a chromatogram from the toxicology screening performed on the patient’s plasma (Appendix 1B). What was the cause of the patient’s severe condition—i.e., with what substance was he intoxicated?
To determine the cause of the intoxication, the mentioned chromatograms will help us. From theory, we know that the retention time (tR) can be used to identify an unknown substance. Therefore, we will compare the patient’s chromatogram with the chromatogram of the standards and observe whether there are any identical or very similar retention times.

## Slide 3
In this case, we can see two compounds in the chromatogram with similar retention times (tR):
Psilocybin and THC

## Slide 4: Task 2 (quantitative analysis of the sample):
Now that you know the cause of the intoxication, your task is to quantify the substance. Appendix 2 contains a table of measured peak areas (response) for standard substances at six different concentrations. It also lists the toxic and lethal concentration ranges for each substance. Using MS Excel, construct a six-point calibration curve for the noxa (toxic agent) identified in the patient’s plasma and determine its concentration. You will therefore also need the regression equation. Based on the toxic and lethal ranges (Appendix 3), assess the patient’s prognosis. Try to briefly formulate the finding as you would present it to the attending physician.

## Slide 5
We will create calibration curves:
Chart: Psilocibine
| 1E-3 | 0.01 | 0.05 | 0.1 | 0.3 | 0.5
Odezva | 0.02 | 0.27 | 1.1 | 2.3 | 7.1 | 11.5
Chart: THC
| 1E-3 | 0.01 | 0.05 | 0.1 | 0.3 | 0.5
THC Odezva | 0.02 | 0.13 | 0.52 | 1.21 | 3.45 | 5.75

## Slide 6
Using the calibration-curve equation, we calculate the concentration:
We know:
Result: Psilocibine = 0,021 mg/l
THC = 0,002 mg/l
Psilocybin was detected in plasma at a concentration of 0.021 mg/L, which exceeds the toxic range and may be associated with acute psychotropic effects (hallucinations, anxiety, confusion). The THC concentration of 0.002 mg/L is low and of no clinical significance. The patient’s prognosis is favorable with continued supportive and symptomatic treatment; severe intoxication is not expected.

## Slide 7: Task 3 (Chromatographic Method – Overview):
Complete the following text and questions:
Every chromatographic system contains two phases. a) The mobile phase in this task is ____________ (polar / non-polar). b) The stationary phase in the C18 column is ____________ (polar / non-polar).
Which of the substances identified in Task 1 will be retained longer on the reversed phase? Try to explain why. (Consider their polarity.)
THC will be retained longer on the reversed phase because its nonpolar character causes stronger interactions with the nonpolar stationary phase.
Explain the term retention time. What does it tell us about the properties of a given substance?
The retention time is the time that elapses from the moment the sample is injected onto the beginning of the chromatographic column until the moment when the peak maximum of the given compound is reached at the detector.
Which parameter of the chromatogram (peak area, peak height, retention time) a) is related to the amount of substance in the sample? b) is used for its identification?
polar
non-polar
Retention time
Peak area, peak height

## Slide 8
What is the principle of separation in liquid chromatography? (Briefly describe how the individual substances are separated.)
The separation of compounds occurs based on the different affinities of the sample components for the stationary and mobile phases. Substances that interact more strongly with the stationary phase elute from the column more slowly, while those with a higher affinity for the mobile phase elute earlier.
Describe at least one type of interaction between the separated substances and the stationary phase.
For example, hydrophobic interactions – in reversed-phase chromatography (e.g. C18), nonpolar compounds bind to the nonpolar surface of the column.
Give an example of two detectors used in combination with liquid chromatography. Specify what are the advantages of using a mass spectrometric detector.
UV/VIS detector, Fluorescence detector MS: High sensitivity and selectivity; suitable for both qualitative and quantitative analysis
Complete the sentence: “Reversed-phase chromatography is suitable for the separation of ____________ (polar / non-polar) compounds because ____________.”
…the non-polar stationary phase interacts more strongly with them, causing these compounds to be retained longer.
Suggest at least two other examples of how chromatographic methods are used in a clinical or toxicological laboratory.
TDM – therapeutic; determination of methanol, ethanol, etc.
non-polar